## Slide 1: ELEC4544 Final Report Depth estimation application on SLAM robot
TAM YUNG YIP， Wenshuo ZHANG

## Slide 2
Today’s Agent:
Background for the whole project
SLAM Robot with Pretrained Depth Estimation Model in Application
Some former work before the final decision

## Slide 3: Background of SLAM
Difficulty in robotic :
1.Robot don’t know the own position without a map
2.Robot can’t do mapping without knowing its own position
SLAM (Simultaneous Localization and Mapping) technology is developed to solve these problem in the same times (path planning)

## Slide 4: Hardware design
Motor (with encoder count)
Motor driver (capable for driving motor)
Lidar (for mapping and localize its own position)
Battery (enough current provided)
Microcontroller (control car base)
Computer (remote the robot)

## Slide 5: ROS(Robot Operating System) STRUCTURE
Different nodes communication
Different computer communication

## Slide 6: SLAM technology
Main idea : repeat iterations of probabilistic algorithms
1. Lidar to get map data
2. Encoder to locate robot position
3. Coordinate transform of the data obtained to draw a map and update robot position
4. Use algorithm to minimize the errors
(AMCL) use particle filter method to
update the probability of robot position

## Slide 7: What’s our initial idea
What do we need?
Training data
Home but not good quality
Outside
City outside
Model
Same size of input and output
Easy to train
Final target
SLAM: Fast and correct

## Slide 8
Have a try:
Result of the easy U-net

## Slide 9
Encode
Change into pretrained Densenet-169
That is too easy to capture all details
Embed pretrained Model
U-net decoder is good(Real reason is there is no pretrained model for this)
Another problem is that the quality of output is not good enough
We use up sampling together

## Slide 10: Depth camera: Depth estimation
Common SLAM robot method: depth camera
- Pros: easy to have 3D image
- Cons: too expensive

## Slide 11: Monocular depth estimation
Computer vision : deep learning model
U-net structure of CNN
Up-sampling and down-sampling for feature extraction

## Slide 12: Monocular depth estimation
Computer vision : deep learning model
U-net structure of CNN
Up-sampling and down-sampling for feature extraction

## Slide 13: Depth estimation result
Chart: Loss and Val Loss
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25
loss | 1.1474 | 0.8575 | 0.6734 | 0.5995 | 0.569 | 0.4895 | 0.4657 | 0.4366 | 0.4242 | 0.4235 | 0.407 | 0.4137 | 0.3743 | 0.4072 | 0.3721 | 0.3586 | 0.3599 | 0.3524 | 0.3391 | 0.3266 | 0.3039 | 0.3375 | 0.3126 | 0.2834 | 0.3039
Val Loss | 1.3299 | 1.1351 | 1.066 | 0.9968 | 1.3291 | 1.1834 | 0.9609 | 0.7232 | 0.5858 | 0.3437 | 0.318 | 0.3158 | 0.2705 | 0.2473 | 0.2538 | 0.2477 | 0.2338 | 0.2315 | 0.2211 | 0.2277 | 0.2158 | 0.2045 | 0.1995 | 0.1951 | 0.2056

## Slide 15: Depth estimation result
Able to response on the monocular camera in ROS structure
Output as 3D point cloud for visualization
Arrows >> red: nearest , blue: middle , green : farthest

## Slide 16: RESULT :SLAM (remote)
Environment : HW301
1. Able to do SLAM with remote control from keyboard
2. Expected mapping result

## Slide 17: RESULT :apply on SLAM robot